## Slide 1: Digi XBee 3 802.15.4 RF Radio Modules with MicroPython

## Slide 2: Digi XBee3 ZigBee Mesh Kit
3 XBee3 ZigBee SMT RF Modules
3 XBee3 SMT Grove Development Boards
3 USB cables
3 Antennas
SMT=Surface Mount (form factor of RF module)

## Slide 3: Software für die Laborübungen
XCTU: https://www.digi.com/products/embedded-systems/digi-xbee/digi-xbee-tools/xctu
PyCarm mit XBee MicroPython PlugIn: https://www.jetbrains.com/de-de/pycharm/
Python: https://www.python.org/downloads/ mit XBee Python library "digi-xbee"

## Slide 4: Documentation
PDFs on Moodle:
  Digi XBee3 ZigBee RF Module User Guide
    your first reference
    covers all aspects regarding the XBee3 ZigBee module
  Digi MicroPython Programming Guide
    intro to MicroPython for XBee3 (not only for ZigBee)
  Digi XBee3 802.15.4 RF Module User Guide
    only if you use the XBee 3 as 802.15.4 module (labs one and two)
  Digi XBee3 RF Module Hardware Reference Manual
    information on hardware layout and pins
  Digi XBee Grove Development Board User Guide
    information on connectors of the development board
    pins
Web Pages
  https://www.digi.com/resources/documentation/digidocs/90002219/default.htm
  https://xbplib.readthedocs.io/en/latest/index.html
  https://github.com/digidotcom/xbee-micropython
  https://docs.micropython.org/en/latest/index.html

## Slide 5: XBee3 – Operating Mode
The Operating Mode defines how the XBee3 devices communicates with the PC via UART via USB
  the communication over radio always uses 802.15.4 radio frames
  communicating XBee3 devices may use different Operating Modes
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
transparent mode (AT)
  data mode
  command mode
API mode
MicroPython
Software
XCTU
Python
Putty
Software
XCTU
Python
Putty
802.15.4
ZigBee
802.15.4
ZigBee
transparent mode (AT)
  data mode
  command mode
API mode
MicroPython
Operating Modes

## Slide 6: XBee3 – Transparent Mode (AT) – Data Mode
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
UART over 802.15.4
Bytes are buffered and packed into radio frames
Payload of radio frames goes to Serial interface
XCTU: just type chars
XCTU: displays
chars

## Slide 7: XBee3 – Transparent Mode (AT) – Command Mode
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
AT commmands to
read and write parameters
trigger actions
enter command mode with „+++“
return to data mode after period of silence
AT commands in Digi XBee® 3 Zigbee® RF Module

## Slide 8: XBee3 – API Mode
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
API frame of different type to
transmit 802.15.4 radio frame
send AT command
…
API frame of different type to
receive 802.15.4 radio frame
get response to AT command
…
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
Tx Request API frame
contains 802.15.4 radio frame
802.15.4 radio frame
Rx Packet API frame
contains 802.15.4 radio frame
In XCTU: use frame generator tool

## Slide 9: XBee3 – MicroPython via XCTU
XBee
XBee
802.15.4 radio frames
PC
(XCTU)
USB (UART)
PC
(XCTU)
USB (UART)
MicroPython Terminal
MicroPython Interpreter
MicroPython Interpreter
MicroPython Terminal
Python Instruction
return value
Python Instruction
return value
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
xbee.transmit
(destination,payload)
xbee.receive()
source, payload
as dictionary
Interpreter
+ XBee Libraries
Terminal
Interpreter
+ XBee Libraries
Terminal
802.15.4 radio frames

## Slide 10: XBee3 – MicroPython via PyCharm PlugIn
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
(XCTU)
USB (UART)
PyCharm
Execute Python Code
Upload
Python Code
PyCharm
Execute Python Code
Upload
Python Code
STDOUT
STDOUT

## Slide 11: XBee3 – Python
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
API frame of different type to
transmit 802.15.4 radio frame
send AT command
…
API frame of different type to
receive 802.15.4 radio frame
get response to AT command
…
XBee
XBee
802.15.4 radio frames
PC
USB (UART)
PC
USB (UART)
Tx Request API frame
802.15.4 radio frame
Python
send_data_16
(destination, payload)
xbee_message = device.read_data()
(from UART)
Python
Rx Packet API frame

## Slide 12: XCTU – First Configuration and First Communication
connect the three XBee modules to the PC
upload the newest firmware
configure all devices to API mode
configure one device as coordinator (forming network), the others as router/end device (joining network)
configure the intended PAN ID
check "Operating Network Parameters" until association is successful
go to console and try sending packets
  send broadcast packets (64-bit=00 00 00 00 00 00 FF FF, 16-bit=FF FE)
  send direct packets (set 64-bit and 16-bit address)

## Slide 13: XCTU Configuration Parameters
MM (MAC Mode):
  must be equal for devices to understand each other‘s frame
  you won‘t see a difference, XCTU range test only with Digi header
PS (MicroPython Auto Start):
  specifies whether MicroPython code on the device starts automatically after start-up
  turn off or upload empty script if you do not use the device with PyCharm plugin
  turn on when you want to use your device remotely i.e. not connected to a computer
BD (UART Baud Rate): defines the Baud rate over the USB
  default with 9600 Baud is less than data rate over the radio interface and thus the bottleneck
  you may want to set higher values but be careful to remember when connecting the device again
D4: User LED
  you use this for the user LED examples
DB (Last Packet RSSI): not configuration but information
  yields the RSSI (received signal strength indicator) for the last packet
  required for you own range test

## Slide 14: XCTU - MicroPython
switch to MicroPython mode (configure AP parameter)
start MicroPython terminal (under Tools), press return and the Python prompt should appear
try some small commands
  print something
  blink the user LED (GPIO 4/Pin 4)
    https://docs.micropython.org/en/latest/library/machine.Pin.html
    "MicroPython Modules" in MicroPython Guide
  transmit a frame and display it by XCTU
    "Get started with MicroPython" section in the XBee3 ZigBee RF Module User Guide
    "XBee device examples" in the MicroPython Guide
  receive a frame transmitted by XCTU
    "Get started with MicroPython" section in the XBee3 ZigBee RF Module User Guide

## Slide 15: Upload MicroPython – PyCharm PlugIn
install PyCharm and XBee MicroPython PlugIn
  "Use the PyCharm plugin" in the MicroPython guide
repeat the three examples from before
  use the existing XBee MicroPython sample projects
combine the examples and control the blinking frequency of the user LED by sending messages from XCTU